## Slide 1: Lecture 10 Introduction to Zybo, Vivado, Lab #4
Pulse Amplitude Modulation 4 (PAM4)
Xilinx vs. Altera (Intel)
Prerequisites and Platform Support
Hardware and Software Codesign with Zynq
The Zynq-7000 AP SoC Chip architecture
The Zybo Board and Zynq 7000 Chip
Xilinx University Program: Embedded Systems Development using Zynq
The First Five Labs from Xilinx University Program: Embedded Systems Development using Zynq
Altera’s Cyclone V SoC
Lab #4: ZYNQ1-1 to 1-16 and ZYNQ2-1 to 2-16

## Slide 2: References
ZYBO Reference Manual, 2014 (pdf)
The Zynq Book (pdf)
Zynq-7000 All Programmable SoC, Technical Reference Manual, 2015
Zynq-7000 All Programmable S
AMBA™ 3 APB Protocol Overview
7 Series FPGAs SelectIO Resources, User’s Guide, 2015
AXI Reference Guide, Xilinx, 2012

## Slide 3
Xilinx video on PAM4: https://www.xilinx.com/products/technology/high-speed-serial/56g.html

## Slide 4
Xilinx video on PAM4: https://www.xilinx.com/products/technology/high-speed-serial/56g.html

## Slide 5: 56G PAM4 Technology
http://www.xilinx.com/products/technology/high-speed-serial/56g.html
Breaks through the physical limitations of data transmission at 50G+ line rates
PAM4 Modulation as the Way Forward
  PAM4 (or 4-level Pulse Amplitude Modulation) has been recognized as the most scalable multi-level signaling protocol for next-generation line rates, and Xilinx is helping drive 56G PAM4 standardization efforts within both the Optical Internetworking Forum (OIF) and the Institute of Electrical and Electronics Engineers (IEEE).
Paving the Way Forward for Next Generation Ethernet
  Cloud Computing, Industrial IoT, and Software-Defined Networks applications
  Scale 50G, 100G, 400G ports, as well as terabit interfaces

## Slide 6: PAM 4
PAM 4 Signal generated on AWG6020 with 72 GS/s Sample rate.
Tektronix
  http://www.tek.com/blog/time-get-ready-pam4
  Four levels on the eye diagram
http://globaltek.us.com/products/southern-photonics-awg34g/awg3420/

## Slide 7
Intel buys Altera
June 1, 2015
Altera is Number 2 FPGA company in USA after Xilinx

## Slide 8: Top FPGA Companies For 2015-16
https://www.eetimes.com/author.asp?doc_id=1331443

## Slide 9: Top Semiconductor Companies in the World in 2018
https://www.eetimes.com/document.asp?doc_id=1334017&_mc=RSS_EET_EDT&utm_source=newsletter&utm_campaign=link&utm_medium=EETimesMCU-20181204

## Slide 10: Objectives
Introduce Xilinx Zybo Zynq-7000 ARM/FPGA SoC Trainer Board, Rev B
Introduce Xilinx Vivado Design Suite
Introduce Software Development Kit (SDK)
Introduce Concept of System on a Chip (SoC)
Introduce Hardware and Software Co-design
Create SoC embedded systems to utilize FPGA and ARM co-design
Linux Solution on Zynq-7000 All Programmable SoC

## Slide 11: Prerequisites and Platform Support
Familiarity with the Xilinx tool set and design flow
Basic C programming
Basic understanding of processor-based system
Basic Verilog HDL knowledge
Vivado System Edition 2015.2
Xilinx University board – Zybo
Linux

## Slide 12: Distinct Features of Hardware and Software Design
 | Hardware | Software
Design Paradigm | Decomposition in space | Decomposition in time
Resource | Area (#gates, #Slices) | Time (#Cycles)
Flexibility | Must be designed in | Implicit
Parallelism | Implicit | Must be designed in
Modeling | Model ≠ Implementation | Model ≈ Implementation
Reuse | Uncommon | Common
Adapted from ECE699 Course Slides
Prepared by Prof. Kris Gaj of George Mason University

## Slide 13: System Design Flow
Xilinx: Creating the Xilinx Zynq-7000 Extensible Processing Platform
Software
Hardware
© Copyright 2014 Xilinx
Notes: The Zynq-7000 Extensible Processing Platform relies on a familiar tool flow for system architects, software developers as well as hardware designers.

## Slide 14: Traditional Discrete Component Architecture
Source: The Zynq Book
© Copyright 2014 Xilinx

## Slide 15: System on a Chip: the Zynq Chip Architecture
Source: The Zynq Book
© Copyright 2014 Xilinx

## Slide 16: Mapping of an Embedded SoC Hardware Architecture to Zynq
Source: The Zynq Book
© Copyright 2014 Xilinx

## Slide 17: Mapping of an Embedded SoC Hardware Architecture to Zynq
Xilinx: Creating the Xilinx Zynq-7000 Extensible Processing Platform
© Copyright 2014 Xilinx
Notes: Figure 1. Unlike previous chips that combine MPUs in an FPGA fabric, Xilinx’s new Zynq-7000 Extensible Processing Platform device family lets the ARM processor, rather than the programmable logic, run the show.

## Slide 18: Zynq Highlights
Source: Xilinx Video Tutorials
© Copyright 2014 Xilinx

## Slide 19: Basic Design Flow for Zynq SoC
Source: the Zynq Book
© Copyright 2014 Xilinx

## Slide 20: Design Flow for Zynq SoC
Source: Xilinx White Paper: Extensible Processing Platform
© Copyright 2014 Xilinx

## Slide 21: Embedded Design Architecture in Zynq
Processor and peripherals
  Dual ARM® Cortex™ -A9 processors of Zynq-7000 AP SoC
  AXI interconnect
  AXI component peripherals
  Reset, clocking, debug ports
Software platform for processing system
  Bare Metal Applications or OS’s (e.g. Linux, FreeRTOS)
  C language support
  Processor services
  C drivers for hardware
User application
  Interrupt service routines (optional)

## Slide 22: The Zynq-7000 AP SoC Chip Architecture
Up to 1GHz, dual-core, ARM Cortex-A9 MPCore microprocessor
On-Chip memory controllers
Peripherals
ARM AMBA AXI-based interconnect
Programmable Logic

## Slide 23: Zynq-7000 SoC: Processing System and Programmable Logic
Processing System (PS)
  Dual-core ARM® Cortex™-A9 MPCore™ with CoreSight™ up to 1GHz
  Dynamic Memory interface (DMI): DDR3, DDR3L, DDR2, LPDDR2
  High Speed Peripherals: USB 2.0, Gigabit Ethernet, SD/SDIO
  Timers: Public and private
  General interrupt controller (GIC)
  On-chip memory (OCM): ROM and RAM
  Debug controller: CoreSight
Programmable Logic (PL)
  Max Logic Cells/ System Logic Cells (K): 444
  Max Memory (Mb): 26.5
  Max DSP Slices: 2,020
  Max I/O Pins: 250

## Slide 24: The Zynq AP SoC Processing System
PS
  APU
  Memory
  Peripherals
  MIO
PL
  Artix®-7
  CLBs
  BRAM
  DSP
  XADC
  CMT
  SelectIO
Page 27, ug585-Zynq-7000-TRM

## Slide 25: Zynq Architecture Built-in Peripherals
Two USB 2.0 OTG/Device/Host
  OTG: On-The-Go
Two Tri- Mode GigE (10/100/1000)
  GigE: Gigabit Ethernet
Two SD(Secure Digit) /SDIO interfaces
  Memory, I/O and combo cards
Two CAN 2.0Bs, SPIs , I2Cs, UARTs
Four GPIO 32bit Blocks
  54 available through MIO; other available through EMIO
Multiplexed Input/Output (MIO)
  Multiplexed pinout of peripherals and static memories
Extended MIO (EMIO)
  Maps PS peripheral ports to the PL

## Slide 26: Processing System (PS): ZYNQ XC7Z010-1CLG400C Chip
ARM Cortex-A9 processor , 650MHz
Single and double precision Vector Floating Point Unit (VFPU)
Timer and Interrupts; Three watchdog timers
One global timer; Two triple-timer counters
Caches
  32 KB Level 1 4-way set-associative instruction and data caches
  512 KB 8-way set-associative Level 2 cache (shared between the CPUs)
On-Chip Memory
  256 KB on-chip RAM (OCM), On-chip boot ROM
External Memory Interfaces
  16-bit or 32-bit interfaces to DDR3, DDR3L, DDR2, or LPDDR2 memories
  1GB of address space using single rank of 8-, 16-, or 32-bit-wide
  8-bit SRAM data bus with up to 64 MB support
ug585-Zynq-7000-TRM

## Slide 27: PS: ZYNQ XC7Z010-1CLG400C Chip
I/O Peripherals and Interfaces
  Two 10/100/1000 tri-speed Ethernet MAC peripherals with
  Two USB 2.0 OTG peripherals• Intel EHCI compliant USB host
  Two full CAN 2.0B compliant CAN bus interfaces
  Two SD/SDIO 2.0/MMC3.31 compliant controllers
  Two full-duplex SPI ports with three peripheral chip selects
  Two high-speed UARTs (up to 1 Mb/s)
  Two master and slave I2C interfaces
GPIO with four 32-bit banks
  up to 54 bits can be used with the PS I/O
  up to 64 bits connected to the Programmable Logic
  Up to 54 flexible multiplexed I/O (MIO) for peripheral pin assignments
Interconnect
  High-bandwidth connectivity within PS and between PS and PL
  ARM AMBA® AXI based
ug585-Zynq-7000-TRM

## Slide 28: Programmable Logic (PL): Artix-7 FPGA
450MHz Internal Clock
Configurable Logic Blocks (CLB)
  28K Logic Cells, 17,600 Look-up tables (LUT); 35,200 Flip-flops; Cascadeable adders
240 Kb Block RAM
80 DSP Blocks
  18 x 25 signed multiply; 48-bit adder/accumulator; 25-bit pre-adder
Programmable I/O Blocks
  Supports LVCMOS, LVDS, and SSTL; 1.2V to 3.3V I/O
Serial Transceivers
  Up to 16 receivers and transmitters; Supports up to 12.5 Gb/s data rates
Two 12-Bit Analog-to-Digital Converters
  Up to 17 external differential input channels
  One million samples per second maximum conversion rate
ug585-Zynq-7000-TRM

## Slide 29: Zybo Zynq-7000 ARM/FPGA SoC Trainer Board
Digilent
$189
Voucher for Xilinx Vivado Design Suite: Design Edition (One full seat, node locked, device-locked to the Zynq-7000 XC7Z010)
4GB microSD card
Micro USB cable
5V 2.5A switching power supply

## Slide 30: Resources on the Zybo Board
28,000 logic cells
40 KB Block RAM
80 DSP slices
On-chip dual channel, 12-bit, 1 MSPS analog-to-digital converter (XADC)
650 MHz dual-core Cortex™-A9 processor
On-board JTAG programming and UART to USB converter
DDR3 memory controller with 8 DMA channels
512 MB x32 DDR3 w/ 1050Mbps bandwidth
128 Mb Serial Flash w/ QSPI interface
microSD slot (supports Linux file system)
High-bandwidth peripheral controllers: 1G Ethernet, USB 2.0, SDIO

## Slide 31: Resources on the Zybo Board
Low-bandwidth peripheral controller: SPI, UART, I2C
Dual-role (Source/Sink) HDMI port
16-bits per pixel VGA output port
Trimode (1Gbit/100Mbit/10Mbit) Ethernet PHY
OTG USB 2.0 PHY (supports host and device)
External EEPROM (programmed with 48-bit globally unique EUI-48/64™ compatible identifier)
Audio codec with headphone out, microphone and line in jacks
GPIO: 6 pushbuttons, 4 slide switches, 5 LEDs
Six Pmod connectors (1 processor-dedicated, 1 dual analog/digital)

## Slide 32: Zynq 7000 Chip on Zybo Board
XC7Z010T-1CLG400 All Programmable SoC
The Zynq-7000 AP SoC architecture consists of two major sections
PS: Processing system
  Dual ARM Cortex-A9 processor based
  Multiple peripherals
  Hard silicon core
PL: Programmable logic
  Shares the same 7 series programmable logic as
  Artix™-based devices: Z-7010, Z-7015, and Z-7020 (high-range I/O banks only)

## Slide 33: Xilinx University Program: Embedded Systems Development using Zynq
Notes: The Xilinx University Program (XUP) enables academics to introduce and use Xilinx technologies in their curriculum and research. XUP collaborates with application expert academics to develop and deliver top-quality teaching materials. XUP also develops in-house workshop materials, teaching users how to use the tools and technologies in the most efficient ways. These workshop materials are accessible to academics to use in classes in their original forms and/or extend with additional material. XUP also gets actively involved in research projects where Xilinx FPGA technologies are utilized.

## Slide 34: The First Five Labs: Embedded Systems Development using Zynq
From Xilinx University Program Website
Introduction to Embedded System Design using Zynq and Vivado
Lab 1: Simple Hardware Design
Zynq Architecture
Extending the Embedded System into PL
Lab 2: Adding IPs in Programmable Logic
Adding Your Own Peripheral
Lab 3: Creating and Adding Custom IP Software Development Environment
Lab 4: Writing Basic Software Applications
Software Development and Debugging
Lab 5: Software Debugging Using SDK

## Slide 35: ARM Cortex-A9 based Embedded System Design: ZYNQ Lab1 through Lab5
Lab #4 of this class: ZYNQ Labs 1 and 2
Lab #5 of this class: ZYNQ Labs 3 and 4
Lab #6 of this class: ZYNQ Lab 5
ARM
Cortex-A9
DDR3
Memory
Controller
AXI
Interconnect
Block
AXI-BRAM Controller
Memory
GPIO
UART
RS232
DIP Switches
AXI4
AXI4-Lite
AXI4-Lite
GPIO
LED_IP
Push-Buttons
AXI4-Lite
LED
Lab1
Lab2
Lab5
Lab3
BRAM
M_AXI_GP0
Lab4 uses hardware built in Lab3
PS
PL
Timer
© Copyright 2015 Xilinx

## Slide 36: Intel Altera’s Cyclone V SoC Hard Processor System
925 MHz, dual-core ARM® Cortex™-A9 MPCore™ processor
32 KB of L1 instruction cache, 32 KB of L1 data cache
512 KB of shared L2 cache
64 KB of scratch RAM
Multiport SDRAM controller with support for DDR2, DDR3, and LPDDR2 and optional error correction code (ECC) support
8-channel direct memory access (DMA) controller
QSPI flash controller, NAND flash controller with DMA
SD/SDIO/MMC controller with DMA
2x 10/100/1000 Ethernet media access control (MAC) with DMA
2x USB On-The-Go (OTG) controller with DMA
4x I2C controller
2x UART

## Slide 37: Altera’s Cyclone V SoC Hard Processor System
4x I2C controller
2x UART
2x serial peripheral interface (SPI) master peripherals, 2x SPI slave peripherals
Up to 134 general-purpose I/O (GPIO)
7x general-purpose timers
4x watchdog timers

## Slide 38: Lab 4: ZYNQ Lab 1 and Lab 2
Lab #4 Part 1: ZYNQ Lab 1 Use Vivado to Build Embedded Systems, pages ZYNQ1-1 to ZYNQ1-16.
Lab #4 Part 2: ZYNQ Lab 2 Adding IP Cores in PL, pages ZYNQ2-1 to ZYNQ2-16.

## Slide 39: USB-UART Bridge on the Zybo Board
The board definition file takes care of mapping the correct MIO pins to the UART 1 controller and uses the following default protocol parameters: 115200 baud rate, 1 stop bit, no parity, 8-bit character length.
The FT2232HQ is also used as the controller for the Digilent USB-JTAG circuitry, but the USB-UART and USB-JTAG functions behave entirely independent of one another.

## Slide 40: UART1 on MIO48 and MIO49

## Slide 41: Lab #4 Part 1 and Part 2: Build a System and Add Soft IP Cores in PL
Lab #4 Part 1: ZYNQ1-16 Lab 1 to build a customized ARM embedded system
Lab #4 Part 2: ZYNQ2-16 Lab 2 to add soft IP cores in PL
AXI Interconnect Ports are IP cores
To connect ARM core, Zynq, to I/O pins for switches and buttons
ARM hard core
AXI interconnect
soft core
AXI crossbar
switch soft cores
AXI interconnect
soft core
EMIO pins
EMIO pins

## Slide 42
Lab #4 Part 2
Synthesized Design Window