## Slide 1: Lecture 12 Zybo Board Definition, LED IP, Lab 5
Zybo Board
  Resources
  MIO and SelectIO pins
Board Interface Files for Zybo and Vivado
  Board Definition File *.xml file
  Processing System File *.tcl file
  C:\Xilinx\Vivado\2015.2\data\boards\board_parts\zybo\B.3
IP Cores
Lab #5 LED IP and Linker

## Slide 2: MIO Pins for Processing System (PS) on Zybo
Communication between the PS and external interfaces is achieved primarily via the Multiplexed Input/Output (MIO), which provides 54 pins of flexible connectivity
MIO 0 TO MIO 53
Pmod F
SPI Flash
GPIO for LED4
ZYBO Reference Manual

## Slide 3: ENET 0 and USB 0: MIO and SelectIO on the Zybo
ENET 0
USB 0
Notice
  F16
  E17
  L16
Notice the external 50MHz Oscillator
ZYBO Reference Manual

## Slide 4: MicroSD: MIO Pins on the Zybo
ENET 0
USB 0
SDIO 0
UART 1
  MIO 48,49
GPIO
  BTN4, MIO50
  BTN5, MIO51
JTAG

## Slide 5: SelectIO pins for Switches and LEDs on Zybo from PS and PL
LEDs on SelectIO: D18, G14, M15, M14
Slide Switches on SelectIO: T16, W13, P15, G15
Buttons on SelectIO: Y16, V16, P16, R18
LED on MIO in PS: MIO7
Buttons on MIO in PS:
  MIO51, MIO50
ZYBO Reference Manual

## Slide 6: SelectIO pins for HDMI on Zybo
HDMI_CLK_P & _N: H16, H17
HDMI_D1_P & _N : C20, B20
HDMI_D2_P & _N: B19, A20
HDMI_D0_P & _N: D19, D20

## Slide 7: SelectIO pins for VGA on Zybo
ZYBO Reference Manual

## Slide 8: SelectIO pins and EMIO pins for Pmod A to E on Zybo
XADC pins are connected to analog input pins of the PL, 1Volt peak to peak for analog
Hi-Speed pins can be used for high speed differential signals
ZYBO Reference Manual

## Slide 9: The Board Definition Files for Zybo
The Board definition file uses an XML format to define information about system-level boards that use or include Xilinx devices
<ip_name>.xml is IP Bill of Material (BOM) file that keeps track of the current state of the IP, including generated files, computed parameters, and interface information.
<ip_name>.xdc is timing and/or physical constraints file. These files are not present for all IP, and their location varies by IP.
XML files define different interfaces on the board. Interfaces such as Slide Switches, Push Buttons, LEDs, USB-UART, DDR Memory, Ethernet etc.
ps7.tcl file – this file specifies how Zynq Processing System 7_0 is configured on Zybo board.
TCL, Tool Command Language , is a file extension for a script written in TCL.
ug895-vivado-system-level-design-entry
Notes: XDC constraints are a combination of: • Industry standard Synopsys Design Constraints (SDC), and • Xilinx proprietary physical constraints XDC constraints have the following properties: • They are not simple strings, but are commands that follow the Tcl semantic. • They can be interpreted like any other Tcl command by the Vivado Tcl interpreter. • They are read in and parsed sequentially the same as other Tcl commands.

## Slide 10: tcl files
TCL is a file extension for a script written in TCL. TCL (also pronounced tickle) stands for Tool Command Language. TCL files are text files containing TCL scripts.
Tool Command Language (TCL) is a dynamic open source language used for building web and desktop applications. Whether on Windows, Mac OS X, or Linux operating systems, TCL files can be opened and edited by WISH and TCLSH.
ug895-vivado-system-level-design-entry
Notes: XDC constraints are a combination of: • Industry standard Synopsys Design Constraints (SDC), and • Xilinx proprietary physical constraints XDC constraints have the following properties: • They are not simple strings, but are commands that follow the Tcl semantic. • They can be interpreted like any other Tcl command by the Vivado Tcl interpreter. • They are read in and parsed sequentially the same as other Tcl commands.

## Slide 11: The Board Definition Files for Zybo B.3: board.xml, part0_pins, preset
board.xml contains
part0_pins.xml
preset.xml
Notes: XDC constraints are a combination of: • Industry standard Synopsys Design Constraints (SDC), and • Xilinx proprietary physical constraints XDC constraints have the following properties: • They are not simple strings, but are commands that follow the Tcl semantic. • They can be interpreted like any other Tcl command by the Vivado Tcl interpreter. • They are read in and parsed sequentially the same as other Tcl commands.

## Slide 12: The Board Definition Files for Zybo B.3: part0_pins.xml
Nine pins are defined in part0_pins.xml
Notes: XDC constraints are a combination of: • Industry standard Synopsys Design Constraints (SDC), and • Xilinx proprietary physical constraints XDC constraints have the following properties: • They are not simple strings, but are commands that follow the Tcl semantic. • They can be interpreted like any other Tcl command by the Vivado Tcl interpreter. • They are read in and parsed sequentially the same as other Tcl commands.

## Slide 13: The Board Definition Files for Zybo B.3: preset.xml
Default clock frequencies and MIO pin configurations in preset.xml
Notes: XDC constraints are a combination of: • Industry standard Synopsys Design Constraints (SDC), and • Xilinx proprietary physical constraints XDC constraints have the following properties: • They are not simple strings, but are commands that follow the Tcl semantic. • They can be interpreted like any other Tcl command by the Vivado Tcl interpreter. • They are read in and parsed sequentially the same as other Tcl commands.

## Slide 14: Ethernet 0, Enet0, is connected to MIO 16 to 27
Notes: XDC constraints are a combination of: • Industry standard Synopsys Design Constraints (SDC), and • Xilinx proprietary physical constraints XDC constraints have the following properties: • They are not simple strings, but are commands that follow the Tcl semantic. • They can be interpreted like any other Tcl command by the Vivado Tcl interpreter. • They are read in and parsed sequentially the same as other Tcl commands.

## Slide 15: The Board Interface Files for Zybo on Vivado
Board Interface file are listed in the Board tab of the Vivado IP Integrator
When Block Design is opened
Notes: XDC constraints are a combination of: • Industry standard Synopsys Design Constraints (SDC), and • Xilinx proprietary physical constraints XDC constraints have the following properties: • They are not simple strings, but are commands that follow the Tcl semantic. • They can be interpreted like any other Tcl command by the Vivado Tcl interpreter. • They are read in and parsed sequentially the same as other Tcl commands.

## Slide 16: Reusing Your IP
IP from many sources can be packaged and made available in Vivado
All IP available in the Vivado IP Catalog can be used to create IP Integrator designs
Any IP Integrator diagram can be quickly packaged as a single complex IP
IP Packager
Source (C, RTL, IP, etc)
Simulation Models
Documentation
Example Designs
Test Bench
Vivado IP Integrator
Standardized IP-XACT representation
IP Catalog
3rd Party IP
Xilinx IP
User IP

## Slide 17: IP Core with AXI Interface
Example of IP Core with AXI Interface
Custom IP Core

## Slide 18: Create and Package IP
The Create and Package IP wizard allows you to
  Create a template for a new peripheral
  Package the current project
    Only available if project is open
  Package an existing project
The packager allows IP to be included in the IP Catalog for distribution
It uses IP-XACT format
Complete set of files included
  Source code, Constraints, Test Benches (simulation files), documentation

## Slide 19: Generated Template for AXI Lite
HDL implementation of AXI Interface
  32 bit data width
User specifies required number of registers (minimum 4)
Read/write to/from Registers implemented
User logic can be easily connected
User logic can be a hierarchical design

## Slide 20: Generated Template for AXI led

## Slide 21: Files created
component.xml
  IP XACT description
bd
  Block Diagram tcl file
drivers
  SDK and software files (c code)
  Simple register/memory read/write functionality
  Simple SelfTest() code
hdl
  Verilog/VHDL (should be inside project directory
xgui
  GUI tcl file

## Slide 22: Files created

## Slide 23: Edit IP
New Vivado project will open
Template files have been generated and are added to the project
IP can now be edited
  Modify existing template files, add user source files
IP Packager will be open
  Last step is to Package IP
Enable Global Include

## Slide 24: Package IP
Package current project
  Must be open!
  Package generated HDL
Package a directory (another project/source files)
  Option to package as a library core
  Core can be referenced by other IP
  Core not available standalone (Will not display in IP Catalog)
Create New AXI4 Peripheral (previous section)
  Will also need to be packaged
  Similar steps to package for all three flows

## Slide 25: IP-XACT
Industry Standard (IEEE) XML format to describe IP using meta-data
  Ports
  Interfaces
  Configurable Parameters
  Files, documentation
IP-XACT only describes high level information about IP, not low level description, so does not replace HDL or Software.
Enables automatic connection, configuration and integration
Enables integration of 3rd Party IP
  (And Export of your own IP)

## Slide 26: IP Packager
Automatically analyse project/files to determine parameters
Initial Summary
Identifies
  Files
    Source HDL, Testbenches, Documentation,
  Parameters
    Configurable
  Ports
  Interfaces
  Compatibility
Creates GUI Layout for IPI

## Slide 27: Customizing IP for Reuse in IP Packager
© Copyright 2014 Xilinx
Add, Edit or change defaults
Select
Options

## Slide 28: IP repository
The Vivado IP Catalog can be extended by adding additional IP Repositories.
Third party IP, your custom IP, and Xilinx IP are displayed in an identical manner
Packager creates .xml file for the IP
Specify the directory of the user/third party IP repository
  Can be done automatically from packager
  Access from project settings, or IP Catalog
  Displays the IP that has been found
Displays IP in the repository for use in IPI

## Slide 29: IP repository
Choose Project Manager under Vivado Project to see Project Settings
Select IP to see IP Repositories
One IP, led_ip_v1.0, is seen here.

## Slide 30: Lab #5 Part 1: Create Custom IP
Lab #5 Part 1: ZYNQ Lab 3 Use Vivado to Build Embedded Systems, pages ZYNQ3-1 to ZYNQ3-16.
Create and Package IP Wizard
Generates HDL template for
  Slave/Master
    AXI Lite/Full/Stream
Optionally Generates
  Software Driver
    Only for AXI Lite and Full slave interface
  Test Software Application
  AXI4 BFM Example

## Slide 31: Lab #5: Adding Custom IP to the System, XUP ZYNQ 3
The User IP in led_ip_v1_0.v contains a register to store LED data
LEDs themselves do not store data, clocked and reset by PS
AXI Interconnect
AXI4-Lite IP (Slave)
User IP
AXI Transaction logic
(Ready, Valid, Response)
Write Response
Read Addr
Read Data
Write Data
Write Addr
Registers
led_ip_v1_0_S_AXI.v
led_ip_v1_0.v
lab3_user_logic.v
8-bit LED Register
8-bit output
User IP

## Slide 32: AXI4-Lite Slave Custom IP: led_ip_v1_0.v
S_AXI bus- standard template
axi_aclk
  System clock from PS
Axi_aresetn
  System reset from PS
LED[3:0]
  custom port

## Slide 33: Three Levels: led_ip_v1_0.v, led_ip_v1_0_S_AXI, lab3_user_logic
Top: led_ip_v1_0.v – the wrapper
AXI: led_ip_v1_0_S_AXI – Verilog module
  Slave axi4 standard template
Custom: lab3_user_logic – user IP circuit
  8-bit LED register to store data
Under IP Editor for led_ip_v1_0

## Slide 34: AXI4-Lite Slave IP: led_ip_v1_0.v, led_ip_v1_0_S_AXI, lab3_user_logic
lab3_user_logic

## Slide 35: AXI4-Lite Slave IP: module led_ip_v1_0.v
With IP Editor: Run RTL Analysis->Schematic to obtain schematic
4-bit addresses for read s_axi_araddr[3:0] and write s_axi_awaddr[3:0]
8-bit LED LED[7:0], which is a changeable parameter
32-bit read and write data busses

## Slide 36: AXI4-Lite Slave IP: , led_ip_v1_0_S_AXI
This is a standard axi4-lite slave module template
lab3_user_logic module is inserted into this template to create a custom ip

## Slide 37: AXI4-Lite Slave IP: module lab3_user_logic
Create an 8 bit register to store 8-bit data of 32-bit Write Data from axi interconnect
This 8-bit data can be displayed on LEDs
Reset by S_AXI_ARESETN
Clocked by S_AXI_ACLK
Enabled by slv_reg_wren and axi_asaddr==3’h0, 12 bit address
Take 8 bits of 32 bit data on S_AXI_WDATA

## Slide 38: AXI4-Lite Slave IP: lab3_user_logic module, 3 level deep
lab3_user_logic.v under led_ip_v1_0_S_AXI.v
lab3_user_logic

## Slide 39: One Instance of led_ip_v1_0.v with four LEDs
System_led_ip_0_0.v == led_ip_v1_0.v, notice LED[3:0]

## Slide 40: One Instance of led_ip_v1_0.v with four LEDs
System_led_ip_0_0.v == led_ip_v1_0.v, notice LED[3:0]
lab3_user_logic.v is in led_ip_v1_0_S_AXI_inst

## Slide 41: Add constraints file lab3_zybo.xdc
Specify pin positions where LEDs are located.
############################
# On-board LED #
############################
set_property PACKAGE_PIN M14 [get_ports LED[0]]
set_property IOSTANDARD LVCMOS33 [get_ports LED[0]]
set_property PACKAGE_PIN M15 [get_ports LED[1]]
set_property IOSTANDARD LVCMOS33 [get_ports LED[1]]
set_property PACKAGE_PIN G14 [get_ports LED[2]]
set_property IOSTANDARD LVCMOS33 [get_ports LED[2]]
set_property PACKAGE_PIN D18 [get_ports LED[3]]
set_property IOSTANDARD LVCMOS33 [get_ports LED[3]]

## Slide 42: Xilinx Design Constraints (XDC) File for Zybo: Master XDC zip
A zipped file called ZYBO_Master.xdc is available from https://reference.digilentinc.com/zybo:zybo#documentation
Here is the header of ZYBO_Master.xdc

## Slide 43: Xilinx Design Constraints File
The Xilinx® Vivado® Integrated Design Environment (IDE) uses Xilinx Design Constraints (XDC)
It does not support the legacy User Constraints File (UCF) format.
There are key differences between Xilinx Design Constraints (XDC) and User Constraints File (UCF) constraints.
XDC constraints are based on the standard Synopsys Design Constraints (SDC) format.
I/O constraints configure:
  Ports
  Cells connected to ports
Typical constraints include:
  I/O standard
  I/O location

## Slide 44: Lab #5 top Level Circuit
buttons and switches are standard S_AXI4 lite interfaces
led_ip_0 and axi_bram_ctrl_0 are custom IP S_AXI4 interfaces

## Slide 45: Lab #5 top Level Circuit
buttons and switches are standard S_AXI4 lite interfaces
led_ip_0 and axi_bram_ctrl_0 are custom IP S_AXI4 interfaces

## Slide 46: Board Support Package: Block RAM interface for Zynq-7010
AXI Block RAM controller IP, AXI4 Slave
Block RAM IP, Single Port RAM
36Kb block RAM x 60 blocks
True dual-port
Up to 72 bits wide
Configurable as dual 18 Kb block RAMs

## Slide 47: Synchronous Dual-Port and Single-Port RAMs (UG473 7 Series FPGAs Memory)
Two independent access ports
No arbitration between the ports
Write conflict will not cause physical damage but may cause data loss
Zynq-2010 BRAM: 36Kbx60=2.16Mb

## Slide 48: SDK Project: Source files, Linker Script, BSP, Hardware Platform
Software Project
  Source code
  Linker script file
Board Support Package *.bsp
Hardware Platform – system_wrapper
© Copyright 2014 Xilinx
Linker Script

## Slide 49: Linker Properties
The Root panel displays properties for the selected configuration
Shown are the linker options for the Debug configuration
Default settings are fine for simple applications

## Slide 50: Address Management
Embedded processor design requires you to manage the following:
  Address map for the peripherals
  Location of the application code in the memory space
    Block RAM
    SRAM
    External memory (Flash, DDR3)
Memory requirements for your programs are based on the following:
  The amount of memory required for storing the instructions
  The amount of memory required for storing the data associated with the program

## Slide 51: Standard ARM Programming Model
Processing system and programmable logic look the same
  AMBA® and AXI interfaces
  Memory-mapped I/O
  Register access
Consistency for PS and PL = ease of use
Memory map usage: total of 4 GB
  1 GB: DDR RAM
  2 GB: dedicated to PL peripherals
  1 GB: PS peripherals, on-chip memory (OCM), external flash

## Slide 52: Programmer’s View of Programmable Logic
Programmable logic (PL) memory map
  2 GB total space
    1 GB for each AXI master: GP0, and GP1
  Accessible from any processing system (PS) master
    Either Cortex-A9 CPU
    PS DMA engine
    PS peripheral DMA engine
    Ethernet
    USB
    SD/SDIO
Code Snippet
Custom Peripheral

## Slide 53: Address Map: I/O Peripherals (Zynq AP SoC)

## Slide 54: Linker Script
Linker script controls the linking process
  Map the code and data to a specified memory space
  Set the entry point to the executable
  Reserve space for the stack
Required if the design contains a discontinuous memory space

## Slide 55: Linker and Locator Flows
.text1
.data1
.bss1
foo1.o
foo2.o
0xFFFF
0xF000
0xEFFF
0xEF00
0x0000
0x1FFF
0x2000
0xEEFF
Locate
Merged Output Sections
Unused
Executable Image
Code
uninitialized data
Initialized data
.text2
.data2
.bss2
Link
.text
.data
.bss

## Slide 56: Linker Script Generator GUI
Table-based GUI allows you to define the memory space for code and data sections
Launch from Xilinx Tools > Generate Linker Script, or from the C/C++ perspective, right-click on <project> > Generate Linker Script
The tool will create a new linker script (the old script is backed up)

## Slide 57: Linker Script Generator GUI
File location: C:\Xilinx\embedded\2015_2_zynq_labs\lab4\lab4.sdk\lab4\src\lscript.ld

## Slide 58: Lab #5: Writing Basic Software Application and Block RAM
ARM
Cortex-A9
DDR3
Memory
Controller
AXI
Interconnect
Block
AXI-BRAM Controller
Memory
GPIO
UART
RS232
DIP Switches
AXI4
AXI4-Lite
AXI4-Lite
GPIO
LED_IP
Push-Buttons
AXI4-Lite
LED
BRAM
M_AXI_GP0
PS
PL

## Slide 59: Board Support Package Macros in led_ip.h
#ifndef LED_IP_H
#define LED_IP_H
/****************** Include Files ********************/
#include "xil_types.h"
#include "xstatus.h"
#define LED_IP_S_AXI_SLV_REG0_OFFSET 0
#define LED_IP_S_AXI_SLV_REG1_OFFSET 4
#define LED_IP_S_AXI_SLV_REG2_OFFSET 8
#define LED_IP_S_AXI_SLV_REG3_OFFSET 12
#define LED_IP_mWriteReg(BaseAddress, RegOffset, Data) \
Xil_Out32((BaseAddress) + (RegOffset), (u32)(Data))
#define LED_IP_mReadReg(BaseAddress, RegOffset) \
Xil_In32((BaseAddress) + (RegOffset))
XStatus LED_IP_Reg_SelfTest(void * baseaddr_p);

## Slide 60: Xil_Out32(), Xil_in32() in standard_v4_2/src/xil_io.c
/* Performs an input operation for a 32-bit memory location by reading from the
* specified address and returning the Value read from that address.
** @paramAddr contains the address to perform the input operation at.
* @returnThe Value read from the specified input address.
* @noteNone. */
u32 Xil_In32(u32 Addr)
{
return *(volatile u32 *) Addr;
}
/* Performs an output operation for a 32-bit memory location by writing the
* specified Value to the specified address.
* @paramOutAddress contains the address to perform the output operation at.
* @paramValue contains the Value to be output at the specified address.
* @returnNone.
* @noteNone */
void Xil_Out32(u32 OutAddress, u32 Value)
{
*(volatile u32 *) OutAddress = Value;
}
Read (return) content at address Addr
Write (store) Value to content at address Addr

## Slide 61: LED device defined in xparameters.h
/* Definitions for driver LED_IP */
#define XPAR_LED_IP_NUM_INSTANCES 1
/* Definitions for peripheral LED_IP_0 */
#define XPAR_LED_IP_0_DEVICE_ID 0
#define XPAR_LED_IP_0_S_AXI_BASEADDR 0x43C00000
#define XPAR_LED_IP_0_S_AXI_HIGHADDR 0x43C0FFFF

## Slide 62: Lab #5 main() to display slide switch values on LEDs
#include "xparameters.h"
#include "xgpio.h"
#include "led_ip.h"
int main (void)
{
XGpio dip, push;
int i, psb_check, dip_check;
xil_printf("-- Start of the Program --\r\n");
XGpio_Initialize(&dip, XPAR_SWITCHES_DEVICE_ID);
XGpio_SetDataDirection(&dip, 1, 0xffffffff);
XGpio_Initialize(&push, XPAR_BUTTONS_DEVICE_ID);
XGpio_SetDataDirection(&push, 1, 0xffffffff);
while (1) {
psb_check = XGpio_DiscreteRead(&push, 1);
xil_printf("Push Buttons Status %x\r\n", psb_check);
dip_check = XGpio_DiscreteRead(&dip, 1);
xil_printf("DIP Switch Status %x\r\n", dip_check);
LED_IP_mWriteReg(XPAR_LED_IP_S_AXI_BASEADDR,0,dip_check);
for (i=0; i<9999999; i++); }
}

## Slide 63: Three Linker Memory Options: Internal, Block RAM, DDR
ps7_ram_0_S_AXI_BASEADDR, fastest, internal RAM in PS based at 0x00000000 or 0xFFFF0000
ps7_ddr_0_S_AXI_BASEADDR, faster, external DDR memory based at 0x00100000
axi_bram_ctrl_0, slow, very slow – internal block RAM in PL based at 0x40000000

## Slide 64: Memory Clock Speeds: Internal, Block RAM, DDR
650MHz - ps7_ram_0_S_AXI_BASEADDR
525MHz - ps7_ddr_0_S_AXI_BASEADDR
100MHz - axi_bram_ctrl_0

## Slide 65: Heap and Stack with Internal RAM: ps7_ram_0_S_AXI_BASEADDR

## Slide 66: Object Dump
Display information from object files and executables
  Header information, memory map
  Data
  Disassemble code
Section
Name
Loadable Memory Address
Virtual Memory Address
Section Size
Byte alignment
Offset from the beginning of the section header table
arm-xilinx-eabi-objdump –h executable.elf

## Slide 67: Heap and Stack with Internal RAM: ps7_ram_0_S_AXI_BASEADDR
RAM base address 0x00000000
Heap address 0x00008030
Stack address 0x00008430

## Slide 68: Block RAM: axi_bram_ctrl_0

## Slide 69: Heap and Stack with Block RAM: axi_bram_ctrl_0
Block RAM base address 0x40000000
Heap address 0x4000000
Stack address 0x40000400