## Slide 1: Lecture 19 Zybo Base System Design Demo and Color Generation
References
Zybo Base System Design Demo
axi_vdma
axi_dispctrl
VGA Analog Color Generation on Zybo
Bitmap Pixel Frame
DISPLAYDEMO_PATTERN_1:
  image generation
Tweetable Mathematical Art Design Competition
Other images from students at HUST

## Slide 2: References
Vivado Design Suite, AXI Reference Guide UG1037 (v3.0) June 24, 2015, Xilinx
AXI Video Direct Memory Access v6.2, LogiCORE IP Product Guide, Vivado Design Suite, PG020, November 18, 2015, Xilinx
AXI DMA v7.1 LogiCORE IP Product Guide, Vivado Design Suite, PG021, November 18, 2015, Xilinx
AXI4-Stream Video IP and System Design Guide, UG934 (v2.2) April 6, 2016, Xilinx
Getting Started with AXI4-Stream Interface in Zynq Workflow, Mathworks, http://www.mathworks.com/help/hdlcoder/examples/getting-started-with-axi4-stream-interface-in-zynq-workflow.html?s_tid=gn_loc_drop.
axi stream interface by Mohammadsadegh Sadri, http://www.googoolia.com/wp/2014/04/12/lesson-3-axi-stream-interface/.
Zybo Base System Design, Digilient, https://reference.digilentinc.com/zybo:zybo

## Slide 3: Zybo Base System Design
Available from Digilent:
  https://reference.digilentinc.com/reference/programmable-logic/zybo/start: Additional Resources-> Zybo Base System Design(Deprecated)
The block design is for Vivado 2014 and therefore it could not be opened with Vivado 2015 because axi_vdma module was version 6.1 while axi_vdma module in Vivado 2015 is version 6.2
A new block design would need to be created from scratch.
Zybo base design lib folder contains display module axi_dispctrl_1.0.
To add this lib folder to your Vivado project,

## Slide 4: Zybo Base System Design Lib
Zybo base design lib folder contains display module axi_dispctrl_1.0.
To add this lib folder to your Vivado project, copy the lib folder to your Vivado project folder and add this lib to your IP repository.
  The lib will be part of this project even if the project folder is moved.

## Slide 5: A Simplified Zybo Base System Design
Zynq, ARM
axi_vdma_0, AXI Video Direct Memory Access, Xilinx
axi_dspctrl_0, AXI VGA Display Controller, Digilent
AXI General Purpose Port, Synchronization Message Interface
AXI high Performance Port, Memory Interface

## Slide 6: vdma and vga display controller in xparameters.h

## Slide 7: Zybo Base System Design Demo Programs
Base_demo folder of the zybo base system design contains all source files to demonstrate the block design. (zybo_base_system\source\vivado\SDK)
These source programs can be compiled to run under the zybo base system block design.
These source programs can be analyzed to understand vga and hdmi displays as well as audio play.

## Slide 8: Zybo Base System Design Demo

## Slide 9: Zybo Base System Design Example
DisplayDemoInitialize
main
Display Options
DisplayInitialize
DisplayStart
DisplayDemoPrintTest
DISPLAYDEMO_PATTERN_1
MainDemoPrintMenu();
DisplayDemoRun VGA
quit
Yes
No

## Slide 10: AXI Video Direct Memory Access v6.2 axi_vdma
Allow for efficient high-bandwidth access between the AXI4-Stream video interface and the AXI4 interface

## Slide 11: Programming Sequence to configure and start with axi_vdma
1. Write control information to the channel VDMACR register to set interrupt enables if desired, and set VDMACR. RS=1 to start the AXI VDMA channel running.
2. Write a valid video frame buffer start address to the channel START_ADDRESS register 1 to N where N equals Frame Buffers.
3. Write a valid Frame Delay (valid only for Genlock Slave) and Stride to the channel FRMDLY_STRIDE register (Offset 0x58 for MM2S and 0xA8 for S2MM).
4. Write a valid Horizontal Size to the channel HSIZE register (Offset 0x54 for MM2S and 0xA4 for S2MM).
5. Write a valid Vertical Size to the channel VSIZE register (Offset 0x50 for MM2S and 0xA0 for S2MM). This starts the channel transferring video data.

## Slide 12: Example Configuration of Zybo Base System Design: DisplayCtrl , vgaCtrl
typedef struct { //display_ctrl.h
u32 dispCtrlAddr; /*Physical Base address of the disp_ctrl core*/
/*flag indicating if the display controller is being used to drive an HDMI transmitter*/
int fHdmi;
XAxiVdma vdma; /*VDMA driver struct*/
XAxiVdma_DmaSetup vdmaConfig; /*VDMA channel configuration*/
VideoMode vMode; /*Current Video mode*/
/* Array of pointers to the framebuffers */
u32 *framePtr[DISPLAY_NUM_FRAMES];
u32 stride; /* The line stride of the framebuffers, in bytes */
double pxlFreq; /* Frequency of clock currently being generated */
u32 curFrame; /* Current frame being displayed */
DisplayState state; /* Indicates if the Display is currently running */
} DisplayCtrl;
DisplayCtrl hdmiCtrl;
DisplayCtrl vgaCtrl;

## Slide 13: XAxiVdma vdma in xaxivdma.h
/* The XAxiVdma driver instance data. */
typedef struct {
u32 BaseAddr; /**< Memory address for this device */
int HasSG; /**< Whether hardware has SG engine */
int IsReady; /**< Whether driver is initialized */
int MaxNumFrames; /**< Number of frames to work on */
int HasMm2S; /**< Whether hw build has read channel */
int HasMm2SDRE; /**< Whether read channel has DRE */
int HasS2Mm; /**< Whether hw build has write channel */
int HasS2MmDRE; /**< Whether write channel has DRE */
/**< Read Enable for video parameters in * direct register mode */
int EnableVIDParamRead;
int UseFsync; /**< DMA operations synchronized to Frame Sync */
int InternalGenLock; /**< Internal Gen Lock */
XAxiVdma_ChannelCallBack ReadCallBack; /**< Call back for read channel */
XAxiVdma_ChannelCallBack WriteCallBack; /**< Call back for write channel */
XAxiVdma_Channel ReadChannel; /**< Channel to read from memory */
XAxiVdma_Channel WriteChannel; /**< Channel to write to memory */
} XAxiVdma;

## Slide 14: VGA Display Controller axi_dispctrl_v1-00_a from Digilent
S_AXI is connected to Zynq
S_AXIS_MM2S is connected to axi_vdma for data transfer
S_axis_mm2s_tstrb[3:0] is connected to m_axis_mm2s_tkkeep[3:0] axi_vdma
REF_CLK_I and s_axi_aclk are connected to FCLK_CLK0 of Zynq
PXL_CLK drives m_axis_mm2s_aclk
FSYNC is connected to mm2s_fsync of xi_vdma

## Slide 15: DisplayDemoInitialize(): Initialize vgaCtrl in display_ctrl.c
dispPtr->curFrame = 0;
dispPtr->dispCtrlAddr = dispCtrlAddr;
dispPtr->fHdmi = fHdmi;
for (i = 0; i < DISPLAY_NUM_FRAMES; i++)
{
dispPtr->framePtr[i] = framePtr[i];
}
dispPtr->pxlFreq = 0;
dispPtr->state = DISPLAY_STOPPED;
dispPtr->stride = stride;
dispPtr->vMode = VMODE_640x480; //default

## Slide 16: DisplayDemoInitialize(): Initialize VDMA driver in display_ctrl.c
int XAxiVdma_SetFrmStore(XAxiVdma *InstancePtr, u8 FrmStoreNum, u16 Direction)
  FrmStoreNum - - the number of frame store buffers to use.
  Direction - XAXIVDMA_READ/WRITE
Initialize the VDMA Read configuration struct
  dispPtr->vdmaConfig.FrameDelay = 0;
  dispPtr->vdmaConfig.EnableCircularBuf = 1;
  dispPtr->vdmaConfig.EnableSync = 0;
  dispPtr->vdmaConfig.PointNum = 0;
  dispPtr->vdmaConfig.EnableFrameCounter = 0;

## Slide 17: DisplayStart():
#define DISPLAYDEMO_MAX_FRAME (1920*1080)
#define DISPLAYDEMO_STRIDE (1920 * 4)
/ * Configure the VDMA to access a frame with the same dimensions as the current mode */
dispPtr->vdmaConfig.VertSizeInput = dispPtr->vMode.height;
dispPtr->vdmaConfig.HoriSizeInput = (dispPtr->vMode.width) * 4;
dispPtr->vdmaConfig.FixedFrameStoreAddr = dispPtr->curFrame;
/*Also reset the stride and address values, in case the user manually changed them*/
dispPtr->vdmaConfig.Stride = dispPtr->stride;
for (i = 0; i < DISPLAY_NUM_FRAMES; i++)
{
dispPtr->vdmaConfig.FrameStoreStartAddr[i] = (u32) dispPtr->framePtr[i];
}

## Slide 18: DisplayStart():
/*Perform the VDMA driver calls required to start a transfer*/
Status = XAxiVdma_DmaConfig(&(dispPtr->vdma), XAXIVDMA_READ, &(dispPtr->vdmaConfig));
Status = XAxiVdma_DmaSetBufferAddr(&(dispPtr->vdma), XAXIVDMA_READ, dispPtr >vdmaConfig.FrameStoreStartAddr);
Status = XAxiVdma_DmaStart(&(dispPtr->vdma), XAXIVDMA_READ);
Status = XAxiVdma_StartParking(&(dispPtr->vdma), dispPtr->curFrame, XAXIVDMA_READ);

## Slide 19: DisplayStart(): Configure VGA Display Controller to Start axi_vdma Transfer
/* Configure the disp_ctrl core with the display mode timing parameters */
vgaReg[0] = (dispPtr->vMode.width << 16) | (dispPtr->vMode.height);
vgaReg[1] = (dispPtr->vMode.hps << 16) | (dispPtr->vMode.hpe);
vgaReg[2] = (dispPtr->vMode.hpol << 16) | (dispPtr->vMode.hmax);
vgaReg[3] = (dispPtr->vMode.vps << 16) | (dispPtr->vMode.vpe);
vgaReg[4] = (dispPtr->vMode.vpol << 16) | (dispPtr->vMode.vmax);
for (i = 0; i < 5; i++)
{
Xil_Out32(dispPtr->dispCtrlAddr + OFST_DISPLAY_VIDEO_START + (i * 4), vgaReg[i]);
}
/*Enable the disp_ctrl core, which will signal the VDMA to begin transferring data*/
Xil_Out32(dispPtr->dispCtrlAddr + OFST_DISPLAY_CTRL,
(1 <<BIT_DISPLAY_START)); //FSYNC to start axi_vdma

## Slide 20: A Pixel in Portable Network Graphics (PNG) Specification
Alpha – a value to show a pixel’s degree of opacity
  from 0 for transparent
  to 1 for opaque
32-bit pixel color
  8-bit Red
  8-bit Green
  8-bit Blue
  8-bit Alpha
https://www.w3.org/TR/PNG/

## Slide 21: Stride of Frame Buffer Memory
Buffers in video ram generally have a stride (also called pitch) associated with them. The stride is the width of the buffer in bytes. For example, if you have a 1024x768 pixel buffer at 16 bits/pixel (2 bytes/pixel), your stride would be:
1024 pixels * 2 bytes/pixel = 2048 bytes
At 32 bits/pixel (4 bytes/pixel), your stride would be:
1024 pixels * 4 bytes/pixel = 4096 bytes
Stride is important as it delineates where each line of the buffer starts and ends. With a linear buffer format, each line of the buffer follows the previous linearly in video ram:
framebuffer address
0 2048 4096
|---------------|---------------|---------------| ... |---------------|
Stride - This is the number of bytes between the start of one line and the start of another
Stride – The number of bytes for one line
#define DISPLAYDEMO_MAX_FRAME (1920*1080)
#define DISPLAYDEMO_STRIDE (1920 * 4) //1920 pixels and 4 bytes per pixel

## Slide 22: Pixel Color and Frame Definition in display_demo.c and display_demo.h
AXI Video Direct Memory Access v6.2 pg020
//in vga_modes.h
static const VideoMode VMODE_800x600 = {
.label = "800x600@60Hz",
.width = 800,
.height = 600,
.hps = 840,
.hpe = 968,
.hmax = 1055,
.hpol = 1,
.vps = 601,
.vpe = 605,
.vmax = 627,
.vpol = 1,
.freq = 40.0
};
//In display_ctrl.h
#define BIT_DISPLAY_RED 16
#define BIT_DISPLAY_BLUE 0
#define BIT_DISPLAY_GREEN 8

## Slide 23: Pixel Color Packing
AXI Video Direct Memory Access v6.2 pg020
//Pixel Color Packing
wColor = ((u32) fRed << BIT_DISPLAY_RED) | ((u32) fBlue << BIT_DISPLAY_BLUE) | ( (u32) fGreen << BIT_DISPLAY_GREEN); }
//In display_ctrl.h
#define BIT_DISPLAY_RED 16
#define BIT_DISPLAY_BLUE 0
#define BIT_DISPLAY_GREEN 8

## Slide 24: Pixel Color and Frame Definition in display_demo.c and display_demo.h
AXI Video Direct Memory Access v6.2 pg020
X=0
X=799
Y=0
Y=599
Ypos=0
800 pixels x 600 lines
8 bits Alpha
8 bits RED
8 bits BLUE
8 bits GREEN
32 bits per pixel
Byte packing
Stride = 800 pixels x 4 bytes = 3,200 bytes
The number of bytes per line
vMode.width=800
vMode.height=600

## Slide 25: Frame Buffer: u32 vgaBuf[3][1920*1080] – 4 bytes per pixel
//Framebuffers for each display device
#define DISPLAY_NUM_FRAMES 3
#define DISPLAYDEMO_MAX_FRAME 1920*1080
//u32 is 32-bit unsigned integer
u32 vgaBuf[DISPLAY_NUM_FRAMES][DISPLAYDEMO_MAX_FRAME];
0 1 stride-1
1xstride=3200 2*stride-1
Pixels are stored in row by row order to make it easy to display one row at a time.
Each row will need the number of bytes equal to pixel bytes * number of pixels.
Stride is the number of bytes for one row.
The beginning address of a row is therefore equal to the beginning address of the previous row plus stride.
If stride = 800x4=3200, each starting address of frame buffer is N*stride, where N is row number:
0
3200
6400
2xstride=6400

## Slide 26: How to Fill Each Column with the Same Color
wStride = stride/4; //stride = 3200 bytes, wStride=800 bytes
width=800; height=600;
for(xcoi = 0; xcoi < width; xcoi++) { //column by column
iPixelAddr = xcoi;
for(ycoi = 0; ycoi < height; ycoi++) { //row by row
frame[iPixelAddr] = wColor; //same 32-bit color
iPixelAddr += wStride; //32-bit address will increment by 4 bytes
}
}
0 1 stride-1
1xstride=3200 2*stride-1
0
3200
6400
2xstride=6400
iPixelAddr += wStride; //will increment iPixelAddr by 800x4 bytes
iPixelAddr
Ycoi=
0
1
.
.
579
Xcoi=0, 1, ….. 799

## Slide 27: Color Generation: DISPLAYDEMO_PATTERN_1: 7 color bars
u32 vgaBuf[DISPLAY_NUM_FRAMES][DISPLAYDEMO_MAX_FRAME];
void DisplayDemoPrintTest(u32 *frame, u32 width, u32 height, u32 stride, int pattern)
//width = 800; height=600; stride=88x4;
{
u32 xcoi, ycoi;
u32 iPixelAddr;
u32 wStride;
u32 wRed, wBlue, wGreen, wColor;
u32 wCurrentInt;
double fRed, fBlue, fGreen, fColor;
u32 xLeft, xMid, xRight, xInt;
u32 yMid, yInt;
double xInc, yInc;
switch (pattern) //two patterns
Seven color bars = width/7=800/7=114
wStride=stride/4=800
Bar index:
xInt = width/7, number of pixels per bar
Color increment by 2 across pixels in one bar:
xInc is color index = 256/114=2
wCurrentInt is current bar number

## Slide 28: Color Generation: DISPLAYDEMO_PATTERN_1: 7 color bars
Divide the screen into 7 vertical bars
  Each bar has 800/7=114 pixels
Bar 1 is red only; Bar 2 is blue only and Bar 4 is green only
8-bit Color (0-255) is divided with the number of pixels in one bar
  256/114=2
  Initial color is 0 and is incremented by 2 as pixel increases from 0 to 113
Each pixel in one column will get the same color
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Red | ON |  | ON |  | ON |  | ON
Blue |  | ON | ON |  |  | ON | ON
Green |  |  |  | ON | ON | ON | ON

## Slide 29: Color Generation: DISPLAYDEMO_PATTERN_1
AXI Video Direct Memory Access v6.2 pg020
Bar | 1 | 2 | 3 | 4 | 5 | 6 | 7
Red | ON |  | ON |  | ON |  | ON
Blue |  | ON | ON |  |  | ON | ON
Green |  |  |  | ON | ON | ON | ON

## Slide 30: Color Generation: DISPLAYDEMO_PATTERN_1
case DISPLAYDEMO_PATTERN_1:
wStride = stride / 4; /* Find the stride in 32-bit words */
xInt = width / 7; //Seven intervals, each with width/7 pixels; seven color bars 800/7
//256 color intensities per interval. Notice that overflow is handled for this pattern.
xInc = 256.0 / ((double) xInt); //color change based on bar number
fColor = 0.0;
wCurrentInt = 1; //current bar from 1 to 7
for(xcoi = 0; xcoi < width; xcoi++) //column by column, width == number of pixels=800
{
if (wCurrentInt & 0b001) fRed = fColor; else fRed = 0.0; //red for bar 1
if (wCurrentInt & 0b010) fBlue = fColor; else fBlue = 0.0; //blue for bar 2
if (wCurrentInt & 0b100) fGreen = fColor; else fGreen = 0.0; //green for bar 4
/* Just draw white in the last partial interval (when width is not divisible by 7) */
if (wCurrentInt > 7) { wColor = 0x00FFFFFF; } //32 bit color per pixel
else {
wColor = ((u32) fRed << BIT_DISPLAY_RED) | ((u32) fBlue << BIT_DISPLAY_BLUE) | ( (u32) fGreen << BIT_DISPLAY_GREEN); } //color packing
iPixelAddr = xcoi;
// all column will have the same color; height is from 0 to 600
for(ycoi = 0; ycoi < height; ycoi++) { frame[iPixelAddr] = wColor;
/* This pattern is printed one vertical line at a time, so the address must be incremented
* by the stride instead of just 1. */
iPixelAddr += wStride; //address
}
AXI Video Direct Memory Access v6.2 pg020

## Slide 31: Color Generation: DISPLAYDEMO_PATTERN_1
fColor += xInc;
if (fColor >= 256.0)
{
fColor = 0.0;
wCurrentInt++;
}
}
/*
* Flush the framebuffer memory range to ensure changes are written to the
* actual memory, and therefore accessible by the VDMA.
*/
Xil_DCacheFlushRange((unsigned int) frame, DISPLAYDEMO_MAX_FRAME * 4);
break;

## Slide 32: A Better Way to Assign Color with switch statement
Switch statement is much better to describe more than two options.
Compare the if statements and switch statement below, which implement the same function.
if (wCurrentInt & 0b001) fRed = fColor; else fRed = 0.0; //red for bar 1
if (wCurrentInt & 0b010) fBlue = fColor; else fBlue = 0.0; //blue for bar 2
if (wCurrentInt & 0b100) fGreen = fColor; else fGreen = 0.0; //green for bar 4
switch(wCurrentInt) {
case 0b000: {fGreen = 0.0; fBlue = 0.0; fRed = 0.0; break;}
case 0b001: {fGreen = 0.0; fBlue = 0.0; fRed = fColor; break;}
case 0b010: {fGreen = 0.0; fBlue = fColor; fRed = 0.0; break;}
case 0b011: {fGreen = 0.0; fBlue = fColor; fRed = fColor; break;}
case 0b100: {fGreen = fColor; fBlue = 0.0; fRed = 0.0; break;}
case 0b101: {fGreen = fColor; fBlue = 0.0; fRed = fColor; break;}
case 0b110: {fGreen = fColor; fBlue = fColor; fRed = 0.0; break;}
case 0b111: {fGreen = fColor; fBlue = fColor; fRed = fColor; break;}
default: {fGreen = 0.0; fBlue = 0.0; fRed = 0.0; break;}
}

## Slide 33: Tweetable Mathematical Art Design Competition (link)
Write 3 Tweetable (meaning 140 characters or less) function bodies for the red, green and blue values for a 1024x1024 image
Twitter (/ˈtwɪtər/) is an online news and social networking service where users post and interact with messages, "tweets," restricted to 140 characters. Registered users can post tweets.
AXI Video Direct Memory Access v6.2 pg020

## Slide 34: Tweetable Mathematical Art Design Competition: C++ Code
Write 3-byte pixel color into a file.
// NOTE: compile with g++ filename.cpp -std=c++11
// also, if this doesn't work for you, try the alternate char-based version
#include <iostream>
#include <cmath>
#define DIM 1024
#define DM1 (DIM-1)
#define _sq(x) ((x)*(x)) // square
#define _cb(x) abs((x)*(x)*(x)) // absolute value of cube
#define _cr(x) (unsigned short)(pow((x),1.0/3.0)) //cube root
unsigned short RD(int i,int j){
// YOUR CODE HERE
}
unsigned short GR(int i,int j){
// YOUR CODE HERE
}
unsigned short BL(int i,int j){
// YOUR CODE HERE
}
void pixel_write(int,int);
FILE *fp;
int main(){
fp = fopen("MathPic","wb");
fprintf(fp, "P6\n%d %d\n1023\n", DIM, DIM);
for(int j=0;j<DIM;j++)
for(int i=0;i<DIM;i++)
pixel_write(i,j);
fclose(fp);
return 0;
}
void pixel_write(int i, int j){
static unsigned short color[3];
color[0] = RD(i,j)&DM1;
color[1] = GR(i,j)&DM1;
color[2] = BL(i,j)&DM1;
fwrite(color, 2, 3, fp);
}

## Slide 35: Tweetable Mathematical Art Design Competition: Mandelbrot 132 chars
unsigned char RD(int i,int j){
double a=0,b=0,d,n=0;
for(;a*a+(d=b*b)<4&&n++<8192;b=2*a*b+j/5e4+.06,a=a*a-d+i/5e4+.34); return n/4; }
unsigned char GR(int i,int j){ return 2*RD(i,j); }
unsigned char BL(int i,int j){ return 4*RD(i,j);
}

## Slide 36: Tweetable Mathematical Art Design Competition: Ripple in Motion
unsigned char RD(int i,int j){
#define P 6.03
float s=3./(j+250),y=(j+sin((i*i+_sq(j-700)*5)/100./DIM+P)*15)*s;return (int((i+DIM)*s+y)%2+int((DIM*2i)*s+y)%2)*127;}
unsigned char GR(int i,int j){
float s=3./(j+250);
float y=(j+sin((i*i+_sq(j-700)*5)/100./DIM+P)*15)*s;
return (int(5*((i+DIM)*s+y))%2+int(5*((DIM*2-i)*s+y))%2)*127;}
unsigned char BL(int i,int j){
float s=3./(j+250);
float y=(j+sin((i*i+_sq(j-700)*5)/100./DIM+P)*15)*s;
return (int(29*((i+DIM)*s+y))%2+int(29*((DIM*2-i)*s+y))%2)*127;}

## Slide 37: Tweetable Mathematical Art Design Competition: Julia sets
unsigned short red_fn(int i, int j){
#define D(x) (x-DIM/2.)/(DIM/2.)
float x=D(i),y=D(j),X,Y,n=0;while(n++<200&&(X=x*x)+(Y=y*y)<4){x=XY+.36237;y=2*x*y+.32;}return log(n)*256;}
unsigned short green_fn(int i, int j){
float x=D(i),y=D(j),X,Y,n=0;while(n++<200&&(x*x+y*y)<4){X=x;Y=y;x=X*X-Y*Y+.7;y=2*X*Y+.27015;}return log(n)*128;}
unsigned short blue_fn(int i, int j){
float x=D(i),y=D(j),X,Y,n=0;while(n++<600&&(x*x+y*y)<4){X=x;Y=y;x=X*XY*Y+.36237;y=2*X*Y+.32;}return log(n)*

## Slide 38: An Image of 1920x1080 Pixels by Rick Rung, CPE 2018

## Slide 39: Other Images from Students of Huazhong U of Science and Technology